## Slide 1: DEVELOPMENT AND ANALYSIS OF ROBOTIC ARMS FOR HUMANOID MELO
He Shen, Salvador Rojas, Eduardo Molina, Francisco Moxo Galicia, Ni Li
November 13, 2018, ASME IMECE, Pittsburgh, PA
Department of Mechanical Engineering
California State University, Los Angeles
5151 State University Dr, Los Angeles, CA 90032

## Slide 2: Table of Contents
Background
Motivation
Design Process
Development
Experimental Testing
Conclusion

## Slide 3: I. Background-Humanoid
Humanoid Robot
  Designed to look like and interact like a human
  Function in human environments
Robotic arms
  Interact with man made environments
  Similar motion to human arms
  Light weight
Hydraulic and hydraulic hybrid servos
High torque density electromagnetic motors
Atlas
MIT HERMES
Harmonic drive gearboxes
Rollin Justin
ASIMO
ASIMO
Notes: https://upload.wikimedia.org/wikipedia/commons/8/81/Atlas_frontview_2013.jpg
https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=7363420
https://biomimetics.mit.edu/research/mit-hermes-project
Talk more about different actuators
Why not talk about the arm
How is the flow
Give broad info arm of robotic manuipulator
General humanoid robotic manipulator

## Slide 4: I. Background- Robotic Arm
Robotic Arm
  Type of robotic manipulator
  Anthropomorphic functionalities
  Composed of joints and links
Joints
  Revolute Joint (1 DOF)
  Joints need to be actuated
    Usually an electrical rotational motor with mechanical gears
  Harmonic Drive
    No backlash
    Accuracy
    Compact design
    Light weight
    High gear reduction ratios
  Sensors
    Encoders
    Torque Sensors
    Accelerometers and gyroscopes

## Slide 5: Table of Contents
Background
Motivation
Design Process
Development
Experimental Testing
Conclusion

## Slide 6: II. Motivation
High performance robotic arms with lightweight, compact size, force/torque sensing, motion feedback, and precise motion controls are very costly.
There is still a strong need for affordable solutions
Easy manufacturability
Rethink Robotics' Baxter Robot (US$22,000 )
KINOVA JACO2 (US$30,000)
UR Arm ($27,000 to $50,000)
Notes: https://newatlas.com/rethink-robotics-sawyer-robot
https://cobotsguide.com/2016/06/kinova//36680/
This are some common arms used by some shuman oid robots

## Slide 7: Table of Contents
Background
Motivation
Design Process
Development
Experimental Testing
Conclusion

## Slide 8: III. Design Process – Flow Diagram
Natural motion
  Similar range of motion to a human arm
  Joints independently controlled
  Light weight and compact design
Manipulation
  Should be able to use basic facilities or tools designed for humans
  Handle objects up to 2.5 pounds

## Slide 9: III. Design Process – Configuration
Robotic arm designed to mimic the motion of human arms with similar payload handling capabilities
Robotic arm selected to have similar serial link configuration with 5 joints and link lengths similar to those of human arms

## Slide 10: III. Design Process – Joint Design
Each joint composed: Actuator, Harmonic Drive Gearbox, Encoder
Mostly 3D printed parts
  Polylactic Acid (PLA) and Nylon
Notes: Harmonic Drive is not new
Compare to convential harmonic drive
Challenges of printing,
Also heavy
Easy made using printer
Each joint composed:
  Actuator
    DC motor: Joint 1,2 and 3
    Stepper Motor: Joint 4 and 5
  Gearbox
    Harmonic drive mechanism
      high gear reduction ratio
      back drivability,
      compact assembly
      zero-backlash features
    Two Stage: Joint 1,2 and 3
    Single Stage: Joints 4 and 5
    Gear reduction ratio
      = # of teeth on flexible spine, = fixed circular spine and = #teeth on follower spline
      =60 =62 =60
  Sensing unit
Each joint composed:
  Actuator
    DC motor: Joint 1,2 and 3
    Stepper Motor: Joint 4 and 5
  Gearbox
    Harmonic drive mechanism
      high gear reduction ratio
      back drivability,
      compact assembly
      zero-backlash features
    Two Stage: Joint 1,2 and 3
    Single Stage: Joints 4 and 5
    Gear reduction ratio
      𝑟=𝑁_𝑓/(𝑁_1−𝑁_2 )
      𝑁_𝑓= # of teeth on flexible spine, 𝑁_1= fixed circular spine and 𝑁_2= #teeth on follower spline
      𝑁_𝑓=60 𝑁_1=62 𝑁_2=60
      𝑟=900:1
  Sensing unit

## Slide 11: Table of Contents
Background
Motivation
Design Process
Development
Experimental Testing
Conclusion

## Slide 12: IV. Robot Arm Development - Structure
Carbon fiber composite tubing
Weight of arm = 7 pounds
Length of arm = 31 inches
Electronics Harnessed inside Melo
Shoulder joints and elbow joint are driven by brushless DC motors
  Provide 2.5 pound-inches of torque
Wrist joints driven by NEMA 17 stepper motors
  Provide 1.12 pound-inches of torque
Shoulder Joints
Elbow Joint
Wrist Joint
Notes: Cahnge to shoulder and elbow
Change to wrist joints

## Slide 13: IV. Robot Arm Development - Electronics
Master Slave Control scheme
Motor Drivers
  Electronic Speed Controllers
  Stepper Drivers
Motors
  Brushless DC motors
  Stepper Motors
Optical rotary encoder
  Two photo interrupters
  IR LED receiver and transmitter for index
Nano
v3.0
Nano
v3.0
Master
Slave
Motor Drivers
Left-Arm
Motors
Encoders
Mega 2560
ESC
Pololu DRV8825
ESC
ESC
Pololu DRV8825
Nano
v3.0
Notes: Master Slave Control scheme
  Master: Arduino Mega 2560
  Slaves: Arduino Nano
    Send Signals to motor drivers
    Collects encoder data, to send to master
  Powered by 9v Battery
Motor Drivers
  Joint 1,2 and 3: Electronics Speed Controllers (ESC)
  Joint 4 and 5: Pololu DRV 8825 Stepper driver
  Powered by11.1Volt Li-po 5500mAh battery
Optical rotary encoder
  Two photo interrupters
    OPB960L51 from TT Electronics
  IR LED receiver and transmitter for index

## Slide 14: Table of Contents
Background
Motivation
Design Process
Development
Experimental Testing
Conclusion

## Slide 15: V. Experimental Testing
Maximum Payload Test
  Increased payload from 1.5 pounds until 2.75
Gearbox Efficiency Test
  Constant payload of 2.75 lbs.
  Constant Voltage of 11.1 Volts
  Uniform angular speed
  Measuring the maximum current
Gearbox efficiency formula
  = efficiencxy
  = output mechanical power
  = input electrical power
  = output torque for payload at moment arm
  = angular speed (radians/second)
  = voltage in volts = 11.1 volts
  = max current measured in amps

## Slide 16: Experimental Testing – Payload
Start with 1.5 pounds at end of arm
Increase by 0.25 pounds until we get to 2.75 pounds
Able to manipulate with desirable speeds

## Slide 17: V. Experimental Testing – Efficiency
17
(d)
(a)
Joint |  |  |  |  |  |  | (%)
1 | (a) | 7.3 | .39 | 85 | 81 | 34 | 42
 | (d) | 6.5 | .26 | 85 | 72 | 22 | 30
Joint |  |  |  |  |  |  | 
1 | (a) | 7.3 | .39 | 85 | 81 | 34 | 42
 | (d) | 6.5 | .26 | 85 | 72 | 22 | 30
Case 1

## Slide 18: V. Experimental Testing – Efficiency
(e)
(b)
Joint |  |  |  |  |  |  | (%)
2 | (b) | 14 | .49 | 85 | 155 | 42 | 27
 | (e) | 10 | .26 | 85 | 111 | 22 | 20
Joint |  |  |  |  |  |  | 
2 | (b) | 14 | .49 | 85 | 155 | 42 | 27
 | (e) | 10 | .26 | 85 | 111 | 22 | 20
Case 2
Notes: Increased friction

## Slide 19: V. Experimental Testing – Efficiency
(f)
(c)
Joint |  |  |  |  |  |  | (%)
3 | (c) | 10 | .87 | 48 | 113 | 74 | 37
 | (f) | 10 | .63 | 48 | 117 | 53 | 25
Joint |  |  |  |  |  |  | 
3 | (c) | 10 | .87 | 48 | 113 | 74 | 37
 | (f) | 10 | .63 | 48 | 117 | 53 | 25
Case 3

## Slide 20: VI. Conclusion
Designed and manufactured an affordable light-weight arm
  Cost: $695 (USD)
The arm is assembled using mostly 3D printed parts
Demonstrates human like motion and manipulation
Notes: Add future work

## Slide 21: Future Work
Enhancing control system towards autonomous movement
Improving the quality of 3D printing parts through the optimization of 3D printing parameters
Study the effects of heat generation and heat transfer in the joints

## Slide 22: Questions?

## Slide 23: I. Background
Rancho Los Amigos Prosthetic Arm 1963
WABOT-1 1973
Marvin Minsky Arm 1968
Rollin’ Justin 2008
Notes: http://cyberneticzoo.com/teleoperators/1972-rancho-anthropomorphic-manipulator-ram-rancho-los-amigos-hospital-american/
http://cyberneticzoo.com/underwater-robotics/1968-minsky-bennett-arm-marvin-minsky-and-bill-bennett-american/
http://infolab.stanford.edu/pub/voy/museum/pictures/display/1-Robot.htm
https://www.thocp.net/reference/robotics/robotics2.htm
http://www.humanoid.waseda.ac.jp/booklet/photo/WABOT-1-1973.jpg
Talk in general of what robot arm is
Decrecrease emptyness

## Slide 24: Background
Rancho Los Amigos Manipulator
Stanford Arm 1969
Minsky Arm
Silver Arm 1974
Notes: http://cyberneticzoo.com/teleoperators/1972-rancho-anthropomorphic-manipulator-ram-rancho-los-amigos-hospital-american/
http://cyberneticzoo.com/underwater-robotics/1968-minsky-bennett-arm-marvin-minsky-and-bill-bennett-american/
http://infolab.stanford.edu/pub/voy/museum/pictures/display/1-Robot.htm
https://www.thocp.net/reference/robotics/robotics2.htm